## Slide 1: Physical Supply and Use Tables in SEEAW: Main concepts and recording of flows Training Session on the System of Environmental-Economic Accounting for Water (SEEAW) for the Arab Gulf Countries August 25-28, 2008 UN House- Beirut-Lebanon
Michael Vardon
United Nations Statistics Division

## Slide 2: Outline
What do Physical Supply-Use Tables (PSUT) measure?
Concepts
The standard tables of SEEA Water
Supplementary tables
Some data recording issues

## Slide 3: What do PSUT measure?
PSUT describe in physical units
  The exchanges of water between the environment and the economy (abstraction and returns)
  The exchanges of water within the economy (supply and use within the economy)

## Slide 4: Why compiling physical supply and use tables?
They are important because
They allow for the identification of the industries/sectors which put pressure on the environment via extraction and use
They indicate the industries/sectors consuming the most water
Together with monetary data (e.g. from the hybrid accounts), they provide information on water use efficiency and other information useful for water allocation policies

## Slide 5: SEEA Water Overview
Stocks and flows
Economy and environment
This is a complex system, so it is useful to simplify it

## Slide 6: Basic concepts and definitions
Economic activity/
Households
Use
From the environment (abstraction)
From another economic unit
Supply
To the environment (returns)
To another economic unit
Evapotranspiration
Consumption
Consumption

## Slide 7: Water Use
Water use: water intake of industries and households for production and consumption activities. Water Use is the sum of water use within the economy and water use from the environment.
Water use within the economy: water intake for production and consumption activities, which is distributed by industries or households and by the Rest of the World (Imports).
Water use from the environment: water abstracted from water resources, seas and oceans, and precipitation collected by industries and households for production and consumption activities, including rainfed agriculture.

## Slide 8: Water Supply
Water supply: water leaving/flowing-out from an economic unit (Industries, Households and rest of the world). Water supply is the sum of water supply to other economic units and water supply to the environment.
Water supply to the environment (also Water returns): water returned into the environment during a given period of time after use. Returns can be classified according to the receiving media (i.e. water resources and sea water) and to the type of water (e.g. treated water, cooling water, etc.).
Water supply within the economy: water distributed to households and industries (including agriculture) and to the rest of the world (exports). Water supply within the economy is net of losses in distribution.

## Slide 9: Organisation of the Physical Supply-Use Tables
By columns, industries (ISIC Rev.4), households and the Rest of the world
By rows, types of flows
Within the economy the SNA identity “Supply is equal to the Use” holds
They consist of three parts:
  Abstraction (in-flow) of water from the environment to the economy
  Flows within the economy
  Returns (or out-flows) of water from the economy to the environment

## Slide 10: Flows from the environment to the economy

## Slide 11: Flows within the economy
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Flows from the economy to the environment
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Standard PSUT
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Water consumption
Water consumption: part of water use which is not distributed to other economic units and does not return to the environment (to water resources, sea and ocean) because during use it has been incorporated into products, consumed by households or livestock.
It is calculated as a difference between total use and total supply, thus it may include losses due to evaporation occurring in distribution and apparent losses due to illegal tapping and malfunctioning metering
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Supplementary tables and information
The standard tables are the minimum required to meet agreed international standards
Countries can disaggregate the industries and line items to suite individual needs
In many case it is useful to have these data separately identified in the data collection, estimation and compilation processes
If the data are available and of sufficient quality then making it available will enhance it usefulness to decision makers and others

## Slide 16: Supplementary information: Abstraction for own use
Line item 1.a. abstraction for own use:
  Hydroelectric power generation
  Irrigation water
  Mine water
  Urban runoff
  Cooling water
  Other

## Slide 17: Supplementary information: Use of water received from other economic units
Line item 2. Use of water received from other economic units. This can be disaggregated to show:
Water abstracted from the environment for distribution (Distributed water)
Reused water
Wastewater to sewerage
Note that reuse water and wastewater are shown in the standard supply table in line items 4.a and 4.b, respectively.

## Slide 18: Supplementary information: Supply of water to other economic units
Line item 4. Supply of water to other economic units. This can be disaggregated to show:
Water abstracted from the environment for distribution (Distributed water)
Reused water (already shown, item 4.a)
Wastewater to sewerage (already shown, item 4.b)
Desalinated water
Note: Desalinated is included in the use table (line item 1.ii.2) as an abstraction from the environment.

## Slide 19: Additional information: further disaggregation industries
ISIC Rev.4, 1-3
Agriculture (ISIC Rev.4, 1)
Forestry (ISIC Rev.4, 2)
Fishing (ISIC Rev.4, 3)
ISIC Rev.4, 5-33 and 41-43
Mining (ISIC Rev.4, 5-9)
Manufacturing (ISIC Rev.4, 10-32)
ISIC Rev.4, 38,39 and 45-99
Accommodation (ISIC Rev.4, 55)
Food service (ISIC Rev.4, 56)
Public Administration (ISIC Rev.4, 84)
Etc…

## Slide 20: Matrix of transfers within economy
This table is symmetrical.
Is done to match line items 2 and 4 of the supply and use tables
Can be done for each of the components of line items 2 and 4 (i.e. distributed water, reuse water and wastewater to sewerage)
It construction allows you to check that supply = use within the economy.

## Slide 21: Supplementary information: Matrix of flows within the economy
Notes: To see who supplies to whom

## Slide 22: Some data recording issues
Water supply and sewerage services are provided by the same enterprise
Losses in distribution
Water supply industry (ISIC Rev.4, 36): intra-industry transfers
Hydro-electric power (classification enterprises and recording)
Mine ‘de-watering’
Urban run-off
Cooling water

## Slide 23: Enterprises supplying both water and sewerage services
In many countries it is common for one enterprise to provide both natural water (CPC v.2, 1800) and sewerage services (CPC v.2, 941)
In national accounts they will coded according to which product generates the highest value output.
  If it is natural water (CPC v.2, 1800) then it will be Water Supply (ISIC Rev.4, 36).
  If it is sewerage services (CPC v.2, 941) then it will be Sewerage (ISIC Rev.4, 37)
In practice many countries do not separate these industries in the national accounts

## Slide 24: Enterprises supplying both water and sewerage services
In SEEAW these enterprises should be split into two establishments
  One supplying natural water (CPC v.2, 1800) and coded to Water Supply (ISIC Rev.4, 36).
  The other supplying sewerage services (CPC v.2, 941) and coded to Sewerage (ISIC Rev.4, 37)
If they are not split then the flows to and from these industries and to other industries becomes less clear
If they cannot be split then the line items 2 (Use of water from other economic units) and 4 (supply of water to other economic units) should be subdivided to show wastewater to sewerage, reuse water and distributed water (as shown earlier in the presentation)

## Slide 25: Losses in distribution
This is an important policy area and because they are not shown explicitly in the standard supply and use table countries should consider preparing the SEEAW supplementary table on losses in distribution

## Slide 26: Losses in distribution: treatment in standard tables
Water losses in distribution is the volume of water lost during transport through leakages, theft and evaporation between a point of abstraction and a point of use, and between points of use and reuse.
Water supply within the economy is recorded net of water losses in distribution
Losses are recorded in water abstractions from the environment, leakages are recorded in water returns and may be separately recorded under water consumption
The are not explicitly identified

## Slide 27: Supplementary information: Losses in distribution
Notes: To see who supplies to whom

## Slide 28: Water Supply Industry (ISIC Rev.4, 36) – Intra-industry transfers
In some countries different enterprises within the water industry transfers water between themselves
It is important to understand these transfers:
  To avoid double counting
  For policy analysis and decision makers, especially where the price of water varies (for example between regions and between water “wholesalers” and water “retailer”)

## Slide 29: Intra industry supply
Enterprise A
ISIC 36
Enterprise B
ISIC 36
Enterprise D
ISIC 36
Enterprise C
ISIC 36
Water users
120
50
50
40
180
Enterprise E
ISIC 36
140
40
140
Water Supply Industry ISIC Rev.4, 36

## Slide 30: Water Supply Industry (ISIC Rev.4, 36) – Intra-industry transfers
The standard physical supply and use tables do not record these within industry transfers
In countries where this occurs a table showing these should be developed to assist the compilation process and could also be presented as supplementary information
SEEAW does not have a standard table for intra-industry transfer this but one has been developed by UNSD

## Slide 31: Water Supply Industry (ISIC Rev.4, 36) – intra-industry transfers

## Slide 32: Hydro-electric power
Hydro-electric power can be a very large water user in countries. While the water is used it is not consumed
Even though the water is not consumed it is important to record these flows because:
  The water is an essential input to the output of hydro-electricity (and hence an important consideration in decision making and policy analysis)
  This use may take place at the expense of other uses
  The water made available by the infrastructure that supports hydro-electric power and the water available after use are important water sources for industry

## Slide 33: Hydro-electric power: classification of enterprises Is it the Electricity Supply or Water Supply Industry?
The enterprise engaged in the production of hydro-electricity produce two products or outputs
  Electricity (CPC v.2, 171)
  Natural water (CPC v.2, 1800)
In most case the value of the output of energy exceeds the value of the output of water.
As such hydro-electric enterprises are mostly classified to the Electricity Supply Industry (ISIC Rev. 4, 35) in the national accounts of countries
This creates a problem for recording flows in the physical supply and use tables (and hybrid tables)

## Slide 34: The solution to the hydro-electric classification problem
Split the hydro-electricity enterprise into two establishments
  One produces Electricity (CPC v.2, 171) and is classified to Electricity Supply (ISIC Rev. 4, 35)
  The other producers Natural water (CPC v.2, 1800) and is classified to Water Supply (ISIC Rev. 4, 36)
For the establishment classified to ISIC 35 water is recorded as an abstraction for own use, with the volume of water returned equal to the amount abstracted. This results in zero (0) consumption
For the establishment classified to ISIC Rev.4, 36 the water is recorded as an abstraction for distribution

## Slide 35: Recording of water use for Electricity Supply (ISIC Rev.4, 35)
Amount of water abstracted is recorded as an abstraction for own use of surface in the use table
Amount of water returned is recorded is the supply table, as return to surface water
If the amount returned is equal to the amount abstracted then the consumption is zero. If pollution has been added then this would be recorded in the emission account

## Slide 36: Alternative solution to the hydro-electric classification problem
If it is impossible to split the hydro-electricity enterprise into two establishments then:
In the use table the water should be recorded in line item 1 as an abstraction form the environment, however you will not be able to fill in either line item 1.a or 1.b as it is both an abstraction for distribution and an abstraction for own use
In the supply table it will be recorded in line item as a supply to other economic units
It IS NOT recorded in line item 5 as a Total return as it is the first treatment.

## Slide 37: Alternative recording of water use and supply by Electricity Supply (ISIC Rev.4, 35)
Amount of water abstracted is recorded in use table in Total abstraction (item 1) but not in items 1.a or 1.b
Amount of water supplied to other economic units is recorded is the supply table.
If the amount supplied is equal to the amount abstracted then the consumption is zero.
No return to the environment is recorded.

## Slide 38: Mine de-watering
In underground mining water is often pumped out of the mine
It is important to record these flows as
  This may prevent others from using the groundwater
  The groundwater is usually discharge into surface water and may be of a different quality due to natural processes or because of pollutants added
  In arid areas this may disrupt the ecology of the environment
  Once on the surface it can be used by others

## Slide 39: Recording mine de-watering
Amount of water abstracted is recorded as an abstraction for own use of groundwater in the use table
Amount of water returned is recorded is the supply table, as return to surface water
If the amount returned is equal to the amount abstracted then the consumption is zero. If pollution has been added then this would be recorded in the emission account

## Slide 40: Urban run-off
Urban run-off (or storm water) is the precipitation that falls on urban areas that does not evaporate or percolate into the ground but flows via overland flow, underflow or channels or is piped into a water cannel or constructed infiltration facility.
When urban run-off is collected by the sewerage or storm water system the supply and use of this water is recorded against the Sewerage Industry (ISIC Rev. 4, 37)

## Slide 41: Recording of urban run-off
Amount of water abstracted is recorded as an abstraction from other sources in the use table
Amount of water returned is recorded is the supply table, as return to surface water or to sea
If the amount returned is equal to the amount abstracted then the consumption is zero. If pollution has been added then this would be recorded in the emission account

## Slide 42: Cooling water
Cooling water is defined as water which is used to absorb and remove heat
When discharge is may cause thermal pollution or have collected pollutants during use (e.g. if used in metal manufacture)
In some cases industries using water for cooling recycle it “on site”. In other cases it is abstracted and returned to the environment
You need to carefully distinguish which situation is occurring, particularly for large users of cooling water (for example coal fired electricity generators)

## Slide 43: Cooling water Case one: Recycling
Establishment
using water for cooling
Environment
80
100
Cooling pond of establishment
80
Water discharged to pond
and then extracted from pond.
Water abstract from
environment only
to replace the water
consumed by the
industry
Boundary of establishment
Establishment may report an
“intake” of 180 rather than
an abstraction from environment
for own use of 100. This would
be a consumption of 100.Must be
Very careful when interpreting
data from surveys or other sources

## Slide 44: Cooling water Case two: Abstraction and return
Establishment
Using water for cooling
Environment
100
80
Water abstracted from environment and returned
to the environment.
Difference is the consumption.
100 abstracted for own use – 80 returned = 20 consumption

## Slide 45: Cooling water – be careful!
If you misinterpret the situation you may over or under estimate to volume of water consumed
Contact directly the large water users (e.g. coal fired electricity generators to be sure what the situation is

## Slide 46: Conclusion
SEEAW uses existing international classifications (CPC and ISIC) a catagorisation of water flows to describing the flows of water within the environment, and economy as well as between the environment and economy.
Most flows are easily identified and recorded in the standard tables.
The catagoristion of the enterprises in the economy is important, particularly for enterprises hydro-electric power plants and water and sewerage service suppliers.
UNSD is

## Slide 47: Contact details
Michael Vardon
Adviser on Environmental-Economic Accounting
United Nations Statistics Division
New York 10017 USA
Room DC2 1532
Phone: +1 917 367 5391
Fax: +1 917 963 1374
Email: vardon@un.org