## Slide 1: Emission Accounts Training Session on the System of Environmental-Economic Accounting for Water (SEEAW) for the Arab Gulf Countries August 25-28, 2008 UN House- Beirut-Lebanon
Michael Vardon (United Nations Statistics Division)
Michael Nagy (Austrian Environment Agency)

## Slide 2: Outline
What do emission accounts measure?
Concepts
The standard tables of SEEAW
Example of Austria
  Policy uses and indicators

## Slide 3: What do emission accounts measure?
Emission accounts describe, in physical units, flows of pollutants added to wastewater as a result of production and consumption, and flowing into water resources either directly or through the sewage network.

## Slide 4: Why compiling emission accounts
Emission accounts provide information on
  Which activities are responsible for the emission
  How much is being emitted
  Where is being emitted
They are useful for designing policies aimed at reducing pressure on the environment

## Slide 5: Why compiling emission accounts
Since they are linked to the economic accounts (via the hybrid tables), they allow for
  the formulation of cost-effective policies aiming at reducing emissions
  the evaluation of the economic impacts of policies aiming at reducing emissions

## Slide 6: Basic concepts and definitions
Emissions to water are defined as direct release of a pollutant to water as well as the indirect release by transfer to an off-site wastewater treatment plant.
The SEEAW focuses only on the release of substances into water resources through the (direct and indirect) discharge of wastewater into water resources.
The direct discharge of heavy metals and hazardous waste not through wastewater is not covered in the water emission accounts but in the waste accounts.

## Slide 7: Wastewater and pollutants pathways
Sewerage
Other industries
Agriculture
Households
Rest of the world
Water resources and the sea

## Slide 8: Basic concepts and definitions
Point source emissions are those emissions for which the geographical location of the discharge of the wastewater is clearly identified (for example, emissions from wastewater treatment plants, power plants, other industrial establishments)
They are generally easier to measure since the point of emission to the water resources is clearly identified

## Slide 9: Basic concepts and definitions
Non-point (or diffuse) sources of pollution are sources without a single point of origin or a specific outlet into a receiving water body. Pollutants are generally carried off the land by storm-water run-off or may be the result of a collection of individual and small scale polluting activities which for practical reasons cannot be treated as point sources of pollution. The commonly used categories for non-point sources include agriculture and urban areas.

## Slide 10: Scope of emission accounts
Include: | Exclude:
Point sources: Pollutants added to wastewater | Point sources: Discharges of heavy metal and hazardous wastes not contained in wastewater (included in the SEEA waste accounts) Pollutants resulting from in-situ use (e.g. navigation, fishing, etc.)
Non-point sources: Urban runoff Irrigation water and rain-fed agriculture | Non-point sources: All non-point sources except for urban runoff, irrigation water and rain-fed agriculture (included in the quality accounts)

## Slide 11: Basic concepts and definitions
Gross emissions are the pollutants added to the water by an activity, assessed at the point where the wastewater leaves the activity's site (or the dwelling, in the case of households).
Net (or final) emissions correspond to the pollutants discharged into water resources after treatment.
Net emissions= gross emissions if there is no treatment of wastewater

## Slide 12: Emission accounts
Industries, households and the Rest of the world are identified by columns
They record the pollution added to water by an economic unit (and not the total pollution discharged with wastewater)

## Slide 13: Emission accounts
Sewerage
Other industries
Agriculture
Households
Rest of the world
Water resources and the sea
25
5
30
5
25
30
2

## Slide 14: Emission accounts by ISIC 37
Now we can reallocate the emissions by ISIC 37 to the activity responsible for the emission
2

## Slide 15: Emission Accounts
2
30
5
25
27

## Slide 16: Urban runoff
Urban run-off: that portion of precipitation on urban areas that does not naturally percolate into the ground or evaporate, but flows via overland flow, underflow, or channels or is piped into a defined surface water channel or a constructed infiltration facility.
It is generally highly polluted and there is an increasing awareness in the potential danger of discharging it into the environment without treatment.
Notes: <number>
<footer>
<header>
<date/time>
It is important to record the collection and discharge of urban runoff for the following reasons: (i) for management purposes, in order to design policies to reduce its negative impacts on the water resources as urban runoff usually contains relatively high concentrations of pollutants (including bacteria and viruses, solid waste, and toxics such as heavy metals and petroleum-based compounds) which reach receiving waters; (ii) for consistency with the monetary tables, as the value of corresponding services (collection of urban run-offs) is recorded in the economic table; and (iii) for practical reasons, in order to measure consistently the total use and supply of water of ISIC 37: since urban runoff ultimately merges into the return flow from ISIC 37 into the environment, the total return of ISIC 37 in the supply table would include urban runoff in addition to the discharges of wastewater collected from industries and households.

## Slide 17: Urban runoff
Emissions to water in the urban runoff are allocated to the Sewerage industry, ISIC 37 since this is the economic unit responsible for its collection and discharge
Notes: <number>
<footer>
<header>
<date/time>
It is important to record the collection and discharge of urban runoff for the following reasons: (i) for management purposes, in order to design policies to reduce its negative impacts on the water resources as urban runoff usually contains relatively high concentrations of pollutants (including bacteria and viruses, solid waste, and toxics such as heavy metals and petroleum-based compounds) which reach receiving waters; (ii) for consistency with the monetary tables, as the value of corresponding services (collection of urban run-offs) is recorded in the economic table; and (iii) for practical reasons, in order to measure consistently the total use and supply of water of ISIC 37: since urban runoff ultimately merges into the return flow from ISIC 37 into the environment, the total return of ISIC 37 in the supply table would include urban runoff in addition to the discharges of wastewater collected from industries and households.

## Slide 18: Reallocation of emissions
Simplest method:
  Use global abatement rate (the assumption is that there is the same treatment capacity)
Otherwise
  Use information of the treatment type

## Slide 19: Supplementary information (1)
Emission to water resource:
  Surface water (and further disaggregation into artificial reservoirs, lakes, rivers etc.)
  Groundwater
Sludge production
  Total sewage sludge produced (vol.)
  Load in total sewage sludge

## Slide 20: Diffuse emissions
European Harmonised Procedures for Quantification of Nutrient Losses from Diffuse Sources - EUROHARP
Web: http://euroharp.org/index.htm

## Slide 21: Waste Water Emissions in Austria

## Slide 22: Information needs
To answer national policy relevant questions:
  Status, trends, forecasts on emissions and pollution control
Fulfillment of international reporting exercises:
  EU-Urban Waste Water Treatment Directive
  EU-Water Framework Directive
  EPER  PRTR
  Eurostat / OECD Joint Questionnaire on Inland Waters

## Slide 23: Policy demands
“Classical” policy questions:
  What is the % of population connected to collecting system and urban waste water treatment plants?
  Is pollution from urban areas and industry increasing or decreasing?
New Policy questions
  Mostly related to economic considerations (more about these later)

## Slide 24: “Classical” indicators
  Population connected to collecting system and waste water treatment plants
  Waste water quantities (m³) discharged (urban / industry)
  Organic pollutants (BOD / COD) discharged (urban / industry)
  Nutrients (Nitrogen and Phosphorus) discharged (urban / industry)
  (Dangerous substances)

## Slide 25: Characteristics of “classical” waste water indicators
Focus on point sources discharging into surface waters
Policy relevant questions were related to the facts that:
  pollution of surface waters stemmed mainly from point sources
  big potential for improvement of treatment technologies and production processes
Indicators have been the basis for regulations on limitation of discharged pollutants (production sector specific), investments, subsidies and other measures
Indicators have been used for monitoring of progress and assessment of achievement of policy goals

## Slide 26: Indicator: connections to sewerage

## Slide 27: Indicator: Treatment efficiencies and discharges

## Slide 28: New policy questions
Which measures (as e.g. required according to EU-WFD) are the most cost-effective?
  What are the costs to reduce 1 unit of a pollutant discharged from agriculture/industry/urban areas....?
What are the socio-economic costs of polluted waters?
  Health of society
  Economic activities dependent from clean water: e.g. fishery, drinking water production, tourism,...
  Other uncertain effects of loss of healthy environment

## Slide 29: New waste water indicators
Better consideration of diffuse pollution  to consider ALL sources of pollution
Industry aggregation  link with economic indicators
Goals
  identify cost-efficient measures
  assess socio-economic effects
  monitor effects of changed production-technologies

## Slide 30: COD emissions, direct discharges
COD
Manufacture of pulp, paper and paper products (21)
Manufacture of chemicals and chemical products (24)
Sewage and refuse disposal, sanitation and similar activities (90)
Households

## Slide 31: Share of COD emissions

## Slide 32: Nitrogen emissions, direct discharges
Nitrogen (total)
Agriculture, hunting and related service activities (01)
Forestry (02)
Households

## Slide 33: Share of Nitrogen emissions

## Slide 34: Chrome emissions. direct discharges
Chrome
Manufacture of basic metals (27)
Manufacture of other non-metallic mineral products (26)
Manufacture of textiles (17)
Leather (19)

## Slide 35: Share of Chrome emissions

## Slide 36: Data collection
A lot of data collections exists:
  National Accounts
  National reports on the status of the environment
  International reporting obligations (WFD, UWWTD, EPER, etc.)
    Austrian Emissions Inventory: updated once a year with data from regional authorities (for each individual “significant” discharger)

## Slide 37: To further develop emission accounts in Austria
  Demonstrate usefulness to policy makers (e.g. for purposes of EU-WFD)
  Use already existing data collections as far as possible (usually legally binding)
  Modify data collections (and their legal basis) where this is necessary (coverage, sector-specific aggregation)

## Slide 38: Outlook for Austria
Emission accounts project :
  Use of data of the Austrian Emission Inventory on Surface Waters (developed according to EU-WFD, covers “significant” point sources and diffuse sources) for NAMEA-Water Emissions (2004-2005 data)
  Develop methodology for consistent time-series based on WFD-data
Overall goal: Regular update on the basis of WFD-data

## Slide 39: Conclusions
Emission accounts are addressing new policy-relevant questions
Existing data collection systems may contain useful information (e.g. Emissions Register)
May need to set-up specific data collections
Promotion of usefulness of (emission) accounts is very important. They will aide:
  Understanding of the costs and benefits of measures
  discussion with different stakeholders (e.g. agriculture versus industry as polluters of waters)
  monitoring of environmental efficiency
  definition of policy goals

## Slide 40: Contact details
Michael Vardon
Adviser on Environmental-Economic Accounting
United Nations Statistics Division
New York 10017 USA
Room DC2 1532
Phone: +1 917 367 5391
Fax: +1 212 963 1374
Email: vardon@un.org
Michael Nagy
Competency Center for Data Management & Reporting
Umweltbundesamt Austria (Federal Environment Agency)
Spittelauer Laende 5
1090 Vienna
Phone: +43 1 31304 3490
Email: michael.nagy@umweltbundesamt.at